## Slide 1: OST-Gadget: a real-world business planning case study
Introduction
Matthäus Alberding

## Slide 2: The OST Smart Factory is a real-world industrial production environment to showcase applied digitalization
The OST Smart Factory
Rapperswil-Jona
Production of injection-moulded parts.
Buchs
Product management, electronics development, and final assembly.
St. Gallen
Sales and service.

## Slide 3: The smart factory’s product will be the «OST Gadget», a wireless charger for your phone, available in 2022
The OST Gadget
The OST Gadget is a wireless charger for your smartphone or any other Qi-compatible device.

## Slide 4: The electronics is currently externally sourced, an internally developed version produced in Buchs is planned
The OST Gadget
USB-C input
DC 5V/2A, DC 9V/1.67A
Micro-USB input
DC 5V/2A, DC 9V/1.67A
Wireless output
DC 5V/1A (5W), DC 9V/1.1A (10W) charging distance ≤6mm works with all Qi-compatible devices
2 USB-A outputs
DC 5V/1A
LED
Red and blue LED indicating the charging process
Model WPC488-10W

## Slide 5: The housing will be produced in Rapperswil
The OST Gadget
Serial number (DataMatrix-Code)
Printed plastic film (back moulded)
Assembling using snap-in hooks
Integrated NFC-chip
Connection by USB-C or Micro-USB
Housing possible in different colors

## Slide 6: The housing will be produced by injection moulding
The OST Gadget
Upper and lower housing are produced in a family tool injection mold
Rubber studs are produced separately
Transport in thermo-formed trays

## Slide 7: Final assembly will be done in Buchs
The OST Gadget
Electronics quality check
Upper housing parts
Lower housing parts and electronics
Press
Output

## Slide 8: Currently, the material cost is around 8CHF/pc plus 50kCHF fixed cost
The OST Gadget
Chart: 
| Variable cost, per pc at 2500 pcs
Electronics | 5.45
Printed plastic film | 2.26
NFC chip | 0.25
(estimated)
The cost for the injection moulding tools is estimated 50’000 CHF
The variable cost for material is currently around 8CHF/pc
The fixed cost for material is currently around 50’000 CHF

## Slide 9: Wireless charging is only the beginning, many more features could be added
The OST Gadget
Use the NFC chip for data exchange?
Adapt the charging behavior to phone model etc.?
Collect data on charger usage?
…?
?
?
?
?
?
?
Waterproof flash drive, reading and writing via OST Gadget?
Heating a coffee mug?

## Slide 10: Any future OST Gadget must meet the OST Gadget’s requirements
The OST Gadget
Useful
The product must be useful – you need to want to have it!
More than an app
The function of the product must not be replaceable by an app.
Sustainable
The product must be sustainable – no batteries, use of recycled materials, etc.
Representing OST
The product needs to show the competencies of OST.
Suitable for smart factory
It must be feasible to produce the product in the smart factory’s infrastructure. Production of variants (e.g. multiple housing colors) must be possible. Simple assembly is a priority.
Realizable
Product cost and time to market must be reasonable.

## Slide 11: Your task is to scout business opportunities for a future version of the OST Gadget
Case Study «OST Gadget»
Your task is to come up with a proposal for a future OST Gadget, making use of the opportunities of digitalization.
Your proposal can be either:
A data-driven service based on the wireless charger (e.g. adapting charging behavior)
An extension or evolution of the wireless charger (e.g. mug heater)
A completely new gadget
Any idea must meet the OST Gadget’s requirements listed before.
2.0

## Slide 12: The case study is structured into 6 steps
Case Study «OST Gadget»
Analyze your market
In the teams, do a market analysis for your business idea.
Create your marketing strategy
In the teams, do a SWOT analysis and create a marketing strategy for your business idea.
Define your marketing mix
In the teams, define the marketing mix and do a forecast for your business idea.
Present your results
In the teams, present your results in a final presentation to the class. Submit your slides as a pre-read 2 weeks in advance.
2.0
Develop your idea
Individually, come up with your business idea for a future OST Gadget. Prepare a short presentation of your idea (“elevator pitch”).
Convince your peers
Present your ideas to the class. Teams of 3-4 students will be formed around the most popular ideas.
4
2
1
3
5
6