## Slide 1: OST-Gadget: a real-world business planning case study
M. Alberding, 07/2022
workshop version

## Slide 2: The OST Smart Factory is a real-world industrial production environment to showcase applied digitalization
What is the «OST Gadget»?
Rapperswil-Jona
Production of injection-moulded parts.
Buchs
Product management, electronics development, and final assembly.
St. Gallen
Sales and service.
Notes: RJ: Verantwortung für Produktion Spritzgussteile (sehr innovative Infrastruktur)
BU: Produktverantwortung, Elektronikentwicklung und Endmontage; «Business Unit» und RJ ist Teilezulieferer
SG: Verkauf und Service
Alles vollvernetzt und digital integriert über SAP etc.
Story: Task force -> Transparenz (wieviele haben wir, wann laufen wir wo trocken) und Nachverfolgbarkeit (brokerware)

## Slide 3: The smart factory’s product is the «OST Gadget», a wireless charger for your phone
What is the «OST Gadget»?
The OST Gadget is a wireless charger for your smartphone or any other Qi-compatible device.

## Slide 4: The electronics is currently externally sourced, an internally developed version is planned
What is the «OST Gadget»?
USB-C input
DC 5V/2A, DC 9V/1.67A
Micro-USB input
DC 5V/2A, DC 9V/1.67A
Wireless output
DC 5V/1A (5W), DC 9V/1.1A (10W) charging distance ≤6mm works with all Qi-compatible devices
2 USB-A outputs
DC 5V/1A
LED
Red and blue LED indicating the charging process
Model WPC488-10W

## Slide 5: The housing is produced in Rapperswil
What is the «OST Gadget»?
Serial number (DataMatrix-Code)
Printed plastic film (back moulded)
Assembling using snap-in hooks
Integrated NFC-chip
Connection by USB-C or Micro-USB
Housing possible in different colors

## Slide 6: The housing is produced by injection moulding
What is the «OST Gadget»?
Upper and lower housing are produced in a family tool injection mold
Rubber studs are produced separately
Transport in thermo-formed trays
Notes: Story aus dem Leben: Spritzguss

## Slide 7: Final assembly is done in Buchs
What is the «OST Gadget»?
Electronics quality check
Upper housing parts
Lower housing parts and electronics
Press
Output
Notes: - Montage in HLF inkl. Qualitätsprüfung (automatisierte Sichtprüfung)

## Slide 8: Currently, the material cost is around 8CHF/pc plus 50kCHF fixed cost
What is the «OST Gadget»?
Chart: 
| Variable cost, per pc at 2500 pcs
Electronics | 5.45
Printed plastic film | 2.26
NFC chip | 0.25
The cost for the injection moulding tools is 50’000 CHF
The variable cost for material is currently around 8CHF/pc
The fixed cost for material is currently around 50’000 CHF
Assume a depreciation period of 7 years

## Slide 9: Wireless charging is only the beginning, many more features could be added
What is the «OST Gadget»?
Use the NFC chip for data exchange?
Adapt the charging behavior to phone model etc.?
Collect data on charger usage?
…?
?
?
?
?
?
?
Waterproof flash drive, reading and writing via OST Gadget?
Heating a coffee mug?
Notes: Ladegerät nur der erste Schritt – wie geht es weiter? Das ist genau die Frage, auf die Sie eine Antwort geben sollen.
Ein paar Ideen, die auf dem Tisch liegen (im Sinne Brainstorming).
Auf der einen Seite Richtung Daten, auf der anderen Seite Richtung Hardware
Technische Machbarkeit?

## Slide 10: Any future OST Gadget must meet the OST Gadget’s requirements
What is the «OST Gadget»?
Useful
The product must be useful – you need to want to have it!
More than an app
The function of the product must not be replaceable by an app.
Sustainable
The product must be sustainable – no batteries, use of recycled materials, etc.
Representing OST
The product needs to show the competencies of OST.
Suitable for smart factory
It must be feasible to produce the product in the smart factory’s infrastructure. Production of variants (e.g. multiple housing colors) must be possible. Simple assembly is a priority.
Realizable
Product cost and time to market must be reasonable.

## Slide 11: Your task is to scout business opportunities for a future version of the OST Gadget
What is the task of the case study?
Your task is to come up with a proposal for a future OST Gadget, making use of the opportunities of digitalization.
Your proposal can be either:
A data-driven service based on the wireless charger (e.g. adapting charging behavior)
An extension or evolution of the wireless charger (e.g. mug heater)
A completely new gadget
Any idea must meet the OST Gadget’s requirements listed before.
2.0
Notes: Ihre Aufgabe: eine Geschäftsidee für die nächste Generation des Gadgets
Sollte sich im Umfeld Digitalisierung bewegen, d.h. «smart product or service» -> konkret:
  Reiner Service mit Daten, ggf. mit angepasster Elektronik
  Weiterentwicklung der Hardware (mug heater / USB stick)
  Ganz anderes Gadget